## Slide 1
Bloodborne Pathogens
Notes: This presentation is designed to assist trainers conducting OSHA 10-hour General Industry outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of 1970 or for any standards issued by the U.S. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the U.S. Department of Labor.
This presentation does not fulfill the employer’s training obligations under 29 CFR 1910.1030.

## Slide 2: Introduction
Approximately 5.6 million workers in health care and other facilities are at risk of exposure to bloodborne pathogens such as human immunodeficiency virus (HIV – the virus that causes AIDS), the hepatitis B virus (HBV), and the hepatitis C virus (HCV)
OSHA’s Bloodborne Pathogens standard prescribes safeguards to protect workers against the health hazards from exposure to blood and other potentially infectious materials, and to reduce their risk from this exposure
Notes: 29 CFR 1910.1030
“Bloodborne pathogens” means pathogenic microorganisms that are present in human blood and can cause disease in humans. These pathogens include among others hepatitis B virus (HBV), which causes hepatitis B; human immunodeficiency virus (HIV), which causes AIDS; hepatitis C virus and other pathogens, such as those that cause malaria.
“Other potentially infectious materials” means:
The following human body fluids: semen, vaginal secretions, cerebrospinal fluid, synovial fluid, pleural fluid, pericardial fluid, peritoneal fluid, amniotic fluid, saliva in dental procedures, any body fluid that is visibly contaminated with blood, and all body fluids in situations where it is difficult or impossible to differentiate between bodily fluids;
Any unfixed tissue or organ (other than intact skin) from a human (living or dead); and
HIV-containing cell or tissue cultures, organ cultures, and HIV- or HBV-containing culture medium or other solutions; and blood, organs, or other tissues from experimental animals infected with HIV or HBV.

## Slide 3: Who is covered by the standard?
All employees who could be “reasonably anticipated” as the result of performing their job duties to face contact with blood and other potentially infectious materials
“Good Samaritan” acts such as assisting a co-worker with a nosebleed would not be considered occupational exposure
Notes: OSHA’s Bloodborne Pathogens standard, 29 CFR 1910.1030, does not apply to construction, agriculture or maritime.
The term “reasonably anticipated” contact means potential contact as well as actual contact with blood or other potentially infectious materials.

## Slide 4: Some Workers Who are at Risk
Physicians, nurses and emergency room personnel
Orderlies, housekeeping personnel, and laundry workers
Dentists and other dental workers
Laboratory and blood bank technologists and technicians
Medical examiners
Morticians
Law enforcement personnel
Firefighters
Paramedics and emergency medical technicians
Anyone providing first-response medical care
Medical waste treatment employees
Home healthcare workers
Notes: The scope of the Bloodborne Pathogens standard is not limited to employees in these jobs. The hazard of exposure to infectious materials affects employees in many types of industries and is not restricted to the health care industry.

## Slide 5: How does exposure occur?
Most common: needlesticks
Cuts from other contaminated sharps (scalpels, broken glass, etc.)
Contact of mucous membranes (for example, the eye, nose, mouth) or broken (cut or abraded) skin with contaminated blood
Notes: It is estimated that 600,000 to 800,000 needlestick injuries occur each year in the United States.
“Contaminated sharps” means any contaminated object that can penetrate the skin including, but not limited to, needles, scalpels, broken glass, broken capillary tubes, and exposed ends of dental wires.

## Slide 6: Exposure Control Plan
Identifies jobs and tasks where occupational exposure to blood or other potentially infectious material occurs
Describes how the employer will:
  Use engineering and work practice controls
  Ensure use of personal protective equipment
  Provide training
  Provide medical surveillance
  Provide hepatitis B vaccinations
  Use signs and labels
Notes: 1910.1030(c)(1)(i)
The exposure control plan is the key provision of the standard because it requires the employer to identify individuals who will receive the training, protective equipment, vaccination and other protections of the standard.
For more information, see OSHA Instruction CPL 02-02-069, Enforcement Procedures for the Occupational Exposure to Bloodborne Pathogens Standard, Appendix D, Model Exposure Control Plan.

## Slide 7: Exposure Control Plan
Written plan required
Plan must be reviewed at least annually to reflect changes in:
  tasks, procedures, or assignments which affect exposure, and
  technology that will eliminate or reduce exposure
Annual review must document employer’s consideration and implementation of safer medical devices
Must solicit input from potentially exposed employees in the identification, evaluation and selection of engineering and work practice controls
Plan must be accessible to employees
Notes: 1910.1030(c)(1)(i)
Employees who must be consulted are those non-managerial employees responsible for direct patient care who are potentially exposed to injuries from contaminated sharps.

## Slide 8: Universal Precautions
Treat all human blood and certain body fluids as if they are infectious
Must be observed in all situations where there is a potential for contact with blood or other potentially infectious materials
Notes: 1910.1030(d)(1)
Universal Precautions is an approach to infection control used to protect employees from exposure to all human blood and other potentially infectious materials.
Alternative concepts in infection control are called Body Substance Isolation (BSI) and Standard Precautions. These methods define all body fluids and substances as infectious. These concepts are acceptable alternatives to Universal Precautions provided that facilities using them adhere to all other provisions of this standard.

## Slide 9: Engineering and Work Practice Controls
These are the primary methods used to control the transmission of HBV and HIV
When occupational exposure remains after engineering and work practice controls are put in place, personal protective equipment (PPE) must be used
Notes: 1910.1030(d)(2)
Employers must solicit input from non-managerial employees responsible for direct patient care who are potentially exposed to injuries from contaminated sharps in the identification, evaluation and selection of engineering and work practice controls.

## Slide 10: Engineering Controls
These controls reduce employee exposure by either removing the hazard or isolating the worker. Examples:
Sharps disposal containers
Self-sheathing needles
Safer medical devices
  Needleless systems
  Sharps with engineered sharps injury protections

## Slide 11: Safer Medical Devices
Needless Systems: a device that does not use needles for the collection or withdrawal of body fluids, or for the administration of medication or fluids
Sharps with Engineered Sharps Injury Protections: a non-needle sharp or a needle device used for withdrawing body fluids, accessing a vein or artery, or administering medications or other fluids, with a built-in safety feature or mechanism that effectively reduces the risk of an exposure incident
Notes: 1910.1030(b)

## Slide 12: Work Practice Controls
Wash hands after removing gloves and as soon as possible after exposure
Do not bend or break sharps
No food or smoking in work areas
These controls reduce the likelihood of exposure by altering how a task is performed. Examples:
Notes: Shearing or breaking of contaminated needles is prohibited.
Contaminated needles and other contaminated sharps must not be bent, recapped, or removed except as noted below:
The employer can demonstrate that no alternative is feasible or that such action is required by a specific medical or dental procedure.
Such bending, recapping or needle removal must be accomplished through the use of a mechanical device or a one-handed technique.
Other work practice controls are listed in 1910.1030(d)(2).

## Slide 13: Personal Protective Equipment
Specialized clothing or equipment worn by an employee for protection against infectious materials
Must be properly cleaned, laundered, repaired, and disposed of at no cost to employees
Must be removed when leaving area or upon contamination
Notes: 1910.1030(d)(3)
When there is occupational exposure, PPE must be provided at no cost to the employee to prevent blood or other potentially infectious materials from passing through or contacting the employees’ work or street clothes, undergarments, skin, eye, mouth, or other mucous membranes.

## Slide 14: Examples of PPE
Gloves
Gowns
Face shields
Eye protection
Mouthpieces and resuscitation devices
Notes: The employer must ensure that appropriate PPE in the appropriate sizes is readily accessible at the worksite or is issued to employees. Hypoallergenic gloves, glove liners, powderless gloves, or other similar alternatives must be readily accessible to those employees who are allergic to the gloves normally provided.

## Slide 15: Housekeeping
Location within the facility
Type of surface to be cleaned
Type of soil present
Tasks or procedures being performed
Must develop a written schedule for cleaning and decontamination at the work site based on the:
Notes: 1910.1030(d)(4)(i)
The term “work site” refers not only to permanent fixed facilities such as hospitals, dental/medical offices, etc., but also includes temporary non-fixed workplaces (blood mobiles, ambulances, etc.).

## Slide 16: Housekeeping (cont’d)
After completion of procedures,
When surfaces are contaminated, and
At the end of the work shift
Work surfaces must be decontaminated with an appropriate disinfectant:
Notes: 1910.1030(d)(4)(ii)(A)
Appropriate disinfectants include diluted bleach solution, EPA registered tuberculocides, and sterilants. The lists of these EPA Registered Products are available from the National Antimicrobial Information Network at (800) 447-6349.

## Slide 17: Regulated Waste
Must be placed in closeable, leak-proof containers built to contain all contents during handling, storing, transporting or shipping and be appropriately labeled or color-coded.
Notes: 1910.1030(d)(4)(iii)

## Slide 18: Laundry
Handle contaminated laundry as little as possible and use PPE
Must be bagged or containerized at location where used
No sorting or rinsing at location where used
Must be placed and transported in labeled or color-coded containers
Notes: 1910.1030(d)(4)(iv)
When a facility uses Universal Precautions in the handling of all soiled laundry, alternative labeling or color-coding is sufficient if it permits all employees to recognize that the containers require handling in compliance with Universal Precautions.

## Slide 19: Hepatitis B Vaccination Requirements
Must make available, free of charge at a reasonable time and place, to all employees at risk of exposure within 10 working days of initial assignment unless:
  employee has had the vaccination
  antibody testing reveals immunity
The vaccination must be performed by a licensed healthcare professional
Notes: 1910.1030(f)
Must be provided according to U.S. Public Health Service (USPHS) recommendations. See www.usphs.gov for more information.

## Slide 20: Hepatitis B Vaccination Requirements (cont’d)
Must be provided even if employee initially declines but later decides to accept the vaccination
Employees who decline the vaccination must sign a declination form
Employees are not required to participate in antibody prescreening program to receive vaccination series
Vaccination booster doses must be provided if recommended by the U.S. Public Health Service
Notes: 1910.1030 Appendix A
Hepatitis B Vaccine Declination (Mandatory)
I understand that due to my occupational exposure to blood or other potentially infectious materials I may be at risk of acquiring hepatitis B virus (HBV) infection. I have been given the opportunity to be vaccinated with hepatitis B vaccine, at no charge to myself. However, I decline hepatitis B vaccination at this time. I understand that by declining this vaccine, I continue to be at risk of acquiring hepatitis B, a serious disease. If in the future I continue to have occupational exposure to blood or other potentially infectious materials and I want to be vaccinated with hepatitis B vaccine, I can receive the vaccination series at no charge to me.
This form must be used and cannot be edited.

## Slide 21: What to do if an exposure occurs?
Wash exposed area with soap and water
Flush splashes to nose, mouth, or skin with water
Irrigate eyes with water or saline
Report the exposure
Direct the worker to a healthcare professional
Notes: Treatment should begin as soon as possible after exposure, preferably within 24 hours, and no later than 7 days.

## Slide 22: Post-Exposure Follow-Up
Document routes of exposure and how exposure occurred
Record injuries from contaminated sharps in a sharps injury log, if required
Obtain consent from the source individual and the exposed employee and test blood as soon as possible after the exposure incident
Provide risk counseling and offer post-exposure protective treatment for disease when medically indicated in accordance with current U.S. Public Health Service guidelines
Provide written opinion of findings to employer and copy to employee within 15 days of the evaluation
Notes: 1910.1030(f)(3), (4) & (5)
The requirement to establish and maintain a sharps injury log applies to any employer who is required to maintain a log of occupational injuries and illnesses under 29 CFR 1904.
If the employee consents to baseline blood collection, but does not give consent at that time for HIV serologic testing, the sample must be preserved for at least 90 days.
Current U.S. Public Health Service guidelines: Updated U.S. Public Health Service Guidelines for the Management of Occupational Exposure to HBV, HCV, and HIV and Recommendations for Postexposure Prophylaxis, June 29, 2001.
Call the National Clinician’s Hotline at 1-888-448-4911.

## Slide 23: Biohazard Warning Labels
Warning labels required on:
  Containers of regulated waste
  Refrigerators and freezers containing blood and other potentially infectious materials
  Other containers used to store, transport, or ship blood or other potentially infectious materials
Red bags or containers may be substituted for labels
Notes: 1910.1030(g)(1)
Labels must be predominantly fluorescent orange or orange-red with lettering and symbols in a contrasting color.
Labels must be affixed as close as feasible to the container by string, wire, adhesive, or other method that prevents their loss or unintentional removal.

## Slide 24: Training Requirements
Provide at no cost to employees during working hours
Provide at time of initial assignment to a job with occupational exposure and at least annually thereafter
Additional training needed when existing tasks are modified or new tasks are required which affect the worker’s occupational exposure
Maintain training records for 3 years
Notes: 1910.1030(g)(2) & (h)(2)
Training records must be maintained for 3 years from the date training occurred and include the following information:
Dates of the training sessions
Contents or a summary of the training sessions
Names and qualifications of persons conducting the training
Names and job titles of all persons attending the training sessions

## Slide 25: Training Elements
Copy of the standard
Modes of transmission
Site-specific exposure control plan
Hazard recognition
Use of engineering controls, work practices and PPE
Live question and answer sessions
Notes: 1910.1030(g)(2)(vii) & (viii)
The person conducting the training must be knowledgeable in the subject matter covered by the elements contained in the training program as it relates to the workplace that the training will address.
OSHA does allow video or distance training, but employees still must have access to a “live” person (even if by phone or electronically) to answer questions – i.e., there must be an opportunity for interactive questions and answers with the person conducting the training session.

## Slide 26: Medical Recordkeeping Requirements
Employee’s name and social security number
Employee’s hepatitis B vaccination status
Results of examinations, medical testing, and post-exposure evaluation and follow-up procedures
Health care professional’s written opinion
Information provided to the health care professional
Employee medical records must be kept confidential and not disclosed or reported without the employee’s written consent (unless required by law)
Medical records must be maintained for duration of employment plus 30 years according to OSHA’s rule governing access to employee exposure and medical records
Notes: 1910.1030(h)
Access to employee exposure and medical records: 1910.1020

## Slide 27: Sharps Injury Log
Employers must maintain a sharps injury log for the recording of injuries from contaminated sharps
The log must be maintained in a way that ensures employee privacy and must contain, at a minimum:
  Type and brand of device involved in the incident
  Location of the incident
  Description of the incident
Notes: 1910.1030(h)(5)
The purpose of the sharps injury log is to aid in the evaluation of devices being used in the workplace and to quickly identify problem areas in the facility. It must be reviewed at least annually during the review and update of the Exposure Control Plan.
If the data are made available to other parties (e.g., supervisors, safety committees, employees), any information that could be used to identify the employee must be withheld to protect the employee’s privacy.
The requirement to establish and maintain a sharps injury log applies to any employer who is required to maintain a log of occupational injuries and illnesses under 29 CFR 1904, OSHA’s recordkeeping rule. The sharps injury log must be maintained for the period required by 29 CFR 1904.6.

## Slide 28: Summary
OSHA’s Bloodborne Pathogens standard prescribes safeguards to protect workers against the health hazards from exposure to blood and other potentially infectious materials, and to reduce their risk from this exposure
Implementation of this standard not only will prevent hepatitis B cases, but also will significantly reduce the risk of workers contracting AIDS, Hepatitis C, or other bloodborne diseases
Notes: For more information on Bloodborne Pathogens, see OSHA’s web site at www.osha.gov